## Slide 1: Vehicle performance
Engineering Design Report

## Slide 2: Outline
Design goal
Design flow
Vehicle dynamic study
Susupension kinematics
Validation
Performance analysis
Appendix

## Slide 3: Design concept
Tire data oriented design
Enhance controllability in AutoX
Reduce steering effort

## Slide 4: Design flow
Vehicle dynamic study
Suspension design
Validation
  Lap time simulation
Kinematics design
Load tranfer distribution
Aerodynamic balance
Chassis roll stiffness
Load transfer
Performance analysis
Torque vectoring
Driver input
Set up tuning
  MMM diagram
  Tire data analysis

## Slide 5: Vehicle dynamic study Lap time sim
FSG22 AutoX
TH06: 94.446
TH07: 93.089
Reduce 1.36 sec

## Slide 6: Vehicle dynamic study MMM diagram
Grip:1.75G
Balance: -300Nm @25m/s
Control:292Nm/deg
Stability:2321Nm/deg

## Slide 7: Vehicle dynamic study tire data acquisition
Need to minimize Camber gain

## Slide 8: Suspension kinematics minimize camber change
Outer Wheel
Inner Wheel
Camber Change Within 0.5deg

## Slide 9: Suspension kinematics Front suspension geometry

## Slide 10: Suspension kinematics Rear suspension geometry

## Slide 11: Suspension kinematics Kinematic roll center
Chart: roll center height vs. body roll
| 1 | 0.95000000000000284 | 0.90000000000000568 | 0.84999999999999432 | 0.79999999999999716 | 0.75 | 0.70000000000000284 | 0.65000000000000568 | 0.59999999999999432 | 0.54999999999999716 | 0.5 | 0.45000000000000284 | 0.40000000000000568 | 0.34999999999999432 | 0.29999999999999716 | 0.25 | 0.20000000000000284 | 0.15000000000000568 | 9.9999999999994316E-2 | 4.9999999999997158E-2 | 0
rear | 20.94 | 21.17 | 21.38 | 21.58 | 21.77 | 21.95 | 22.12 | 22.27 | 22.42 | 22.55 | 22.67 | 22.78 | 22.88 | 22.97 | 23.04 | 23.1 | 23.16 | 23.2 | 23.23 | 23.24 | 23.25
front | 20.72 | 20.78 | 20.83 | 20.89 | 20.94 | 20.99 | 21.04 | 21.09 | 21.14 | 21.18 | 21.23 | 21.27 | 21.31 | 21.35 | 21.39 | 21.43 | 21.47 | 21.5 | 21.53 | 21.57 | 21.6 | 21.62 | 21.65 | 21.68 | 21.7 | 21.73 | 21.75 | 21.77 | 21.79 | 21.8 | 21.82 | 21.83 | 21.85 | 21.86 | 21.87 | 21.87 | 21.88 | 21.89 | 21.89 | 21.89 | 21.89
Chart: roll center_lat. vs. body roll
| 1 | 0.95000000000000284 | 0.90000000000000568 | 0.84999999999999432 | 0.79999999999999716 | 0.75 | 0.70000000000000284 | 0.65000000000000568 | 0.59999999999999432 | 0.54999999999999716 | 0.5 | 0.45000000000000284 | 0.40000000000000568 | 0.34999999999999432 | 0.29999999999999716 | 0.25 | 0.20000000000000284 | 0.15000000000000568 | 9.9999999999994316E-2 | 4.9999999999997158E-2 | 0
rear | 191.49 | 181.95 | 172.4 | 162.84 | 153.29 | 143.72 | 134.16 | 124.59 | 115.02 | 105.44 | 95.87 | 86.29 | 76.71 | 67.12 | 57.54 | 47.95 | 38.36 | 28.77 | 19.18 | 9.59 | 0.13
front | 156.69 | 152.87 | 149.05 | 145.21 | 141.37 | 137.53 | 133.67 | 129.81 | 125.94 | 122.07 | 118.19 | 114.31 | 110.42 | 106.52 | 102.62 | 98.72 | 94.81 | 90.89 | 86.97 | 83.05 | 79.12 | 75.19 | 71.25 | 67.31 | 63.37 | 59.42 | 55.48 | 51.52 | 47.57 | 43.61 | 39.66 | 35.7 | 31.73 | 27.77 | 23.8 | 19.84 | 15.87 | 11.9 | 7.93 | 3.97 | 0

## Slide 12: Suspension kinematics Tire attitude
Chart: camber vs. Ay
| 1.8721313631127501 | 1.7813885442443838 | 1.6905478576713757 | 1.5997613136175193 | 1.509662010302816 | 1.4194768480951245 | 1.3300453701585893 | 1.2405360301077153 | 1.1510110024890274 | 1.0621817243865819 | 0.97258274999231442 | 0.88372615379278296 | 0.79553070953602412 | 0.70735853700299145 | 0.6184321050294711 | 0.53020956763170546 | 0.44124823078074799 | 0.35301405887431819 | 0.26477215086058187 | 0.1772265203340978 | 8.8257383620194613E-2
front inner wheel | 1.56 | 1.53 | 1.5 | 1.48 | 1.45 | 1.42 | 1.39 | 1.37 | 1.34 | 1.31 | 1.29 | 1.26 | 1.23 | 1.21 | 1.18 | 1.16 | 1.13 | 1.1 | 1.08 | 1.05 | 1.02 | 1
front outer wheel | 0.47 | 0.49 | 0.52 | 0.54 | 0.57 | 0.59 | 0.62 | 0.64 | 0.67 | 0.69 | 0.72 | 0.74 | 0.77 | 0.79 | 0.82 | 0.84 | 0.87 | 0.89 | 0.92 | 0.95 | 0.97 | 1
rear outer wheel | 0.49 | 0.51 | 0.54 | 0.56 | 0.59 | 0.61 | 0.64 | 0.66 | 0.69 | 0.72 | 0.74 | 0.77 | 0.79 | 0.82 | 0.84 | 0.87 | 0.89 | 0.92 | 0.95 | 0.97
rear inner wheel | 1.52 | 1.49 | 1.47 | 1.44 | 1.41 | 1.39 | 1.36 | 1.34 | 1.31 | 1.28 | 1.26 | 1.23 | 1.21 | 1.18 | 1.15 | 1.13 | 1.1 | 1.08 | 1.05 | 1.02

## Slide 13: Suspension kinematics adaptive steering charateristic
understeer
oversteer
Chart: roll gradient vs. ride height
| -9.2499999999999929 | -8.4999999999999929 | -7.7499999999999929 | -6.9999999999999929 | -6.2499999999999929 | -5.4999999999999929 | -4.7499999999999929 | -3.9999999999999929 | -3.2499999999999929 | -2.4999999999999929 | -1.7499999999999929 | -0.99999999999999289 | -0.24999999999999289 | 0.50000000000000711 | 1.2500000000000071 | 2.0000000000000071 | 2.75 | 3.5 | 4.25 | 5 | 5.75 | 6.5 | 7.25 | 8 | 8.75 | 9.5 | 10.25 | 11 | 11.75 | 12.5 | 13.25 | 14 | 14.75 | 15.5 | 16.25 | 17 | 17.75 | 18.5 | 19.25 | 20 | 20.75 | 21.5 | 22.25 | 23 | 23.75
rear | 560.3994 | 560.3994 | 567.8837 | 567.8837 | 567.8837 | 575.3243 | 582.7196 | 575.3243 | 590.0685 | 582.7196 | 590.0685 | 597.3696 | 597.3696 | 604.6218 | 604.6218 | 611.8239 | 611.8239 | 618.9751 | 618.9751 | 626.0742 | 633.1205 | 633.1205 | 640.1132 | 640.1132 | 653.9346 | 653.9346 | 660.762 | 667.5332 | 674.2476 | 680.9048 | 687.5043 | 694.0459 | 700.5292 | 713.32 | 719.6271 | 732.0642 | 738.194 | 756.2282 | 767.9557 | 779.4479 | 796.2482 | 812.5287 | 833.4408 | 853.4644 | 881.8899 | 908.4676
front | 509.8019 | 516.7332 | 516.7332 | 523.6527 | 523.6527 | 523.6527 | 530.5589 | 530.5589 | 530.5589 | 530.5589 | 537.45 | 537.45 | 537.45 | 544.3247 | 544.3247 | 544.3247 | 551.1814 | 551.1814 | 551.1814 | 551.1814 | 558.0186 | 558.0186 | 564.835 | 564.835 | 564.835 | 571.6292 | 571.6292 | 571.6292 | 578.4 | 578.4 | 585.1461 | 585.1461 | 585.1461 | 591.8665 | 598.5598 | 598.5598 | 605.2251 | 605.2251 | 611.8612 | 618.4673 | 625.0424 | 625.0424 | 638.0959 | 638.0959 | 644.5726 | 657.4222 | 663.7937 | 670.1286
Notes: Design nonlinear motion ratio
Create less understeer when corner entry

## Slide 14: Steering Design flow

## Slide 15: Steering turning radius vs optimum Ackermann percentage
Less understeer when corner entry

## Slide 16: Steering steering geometry design
Notes: Developing a simple model of TH07, we estimated the steering response of steady velocity.
We designed the effective steering arm length curve of TH07, which can fully transform tire situation, also giving a warning to driver that the tire is close to its lateral force limit.

## Slide 17: Steering steering geometry design

## Slide 18: Validation Roll gradient
Constant radius acceleration test

## Slide 19: pitch gradient validation
Designed: 0.47 deg/G

## Slide 20
Validation Aerodynamic balance

## Slide 21
Driver Interpretation
+
-
Ref. Yaw Rate
IMU
Yaw Rate
PID
Difference Torque
Performance analysis Torque vectoring framework
Adjustable
Notes: 俯瞰圖 小車三角形 減緩understeer
This is the framework of our torque vectoring system, according to the vehicle’s speed and steering angle together with our driver’s interpretation, a reference yaw rate is determined then compared to the current yaw rate measured by the IMU. Finally the difference torque is calculated with a PID controller.

## Slide 22: Performance analysis Torque vectoring
Less understeer

## Slide 23: Performance analysis driver input analysis

## Slide 24: Performance analysis driver input analysis

## Slide 25: Performance analysis systematic driver feedback

## Slide 26: Performance analysis set up tuning
ARB rate
spring rate
Steering characteristic
Response
Grip
maneuverability
Driver sensing
TV
Minimize control effort
Notes: 在懸吊中主要調整的參數有，防傾桿扭轉剛性以及彈簧剛性，今年的設計目標為增加懸吊參數的可調性，讓車輛可以根據不同的賽道、車手、輪胎工作溫度…等外在因素去做因鷹的調整，盡量去配合車手的開車風格並開出最佳圈時。 而主要影響輪胎抓地力以及車輛暫態響應的是彈簧剛性，影響操控性以及轉向特性的是防傾桿以及彈簧剛性。 因此，我們會先根據圈時來調整彈簧剛性，在調整至最佳圈時之後，再根據車手回饋調整防傾桿扭轉剛性，配合賽道配置以及車手感受。

## Slide 27: Performance analysis set up tuning
73.3
69.6
58.4
59
Driver feedback:
Too much udersteer
Data analysis:
Too much wear on front tyre
Faster front tire heating
Notes: 在懸吊中主要調整的參數有，防傾桿扭轉剛性以及彈簧剛性，今年的設計目標為增加懸吊參數的可調性，讓車輛可以根據不同的賽道、車手、輪胎工作溫度…等外在因素去做因鷹的調整，盡量去配合車手的開車風格並開出最佳圈時。 而主要影響輪胎抓地力以及車輛暫態響應的是彈簧剛性，影響操控性以及轉向特性的是防傾桿以及彈簧剛性。 因此，我們會先根據圈時來調整彈簧剛性，在調整至最佳圈時之後，再根據車手回饋調整防傾桿扭轉剛性，配合賽道配置以及車手感受。

## Slide 28: Performance analysis set up tuning
60.7
61.1
58.3
58.3
Driver feedback:
Less udersteer
Data analysis:
Less front & rear temperature difference
Notes: 在懸吊中主要調整的參數有，防傾桿扭轉剛性以及彈簧剛性，今年的設計目標為增加懸吊參數的可調性，讓車輛可以根據不同的賽道、車手、輪胎工作溫度…等外在因素去做因鷹的調整，盡量去配合車手的開車風格並開出最佳圈時。 而主要影響輪胎抓地力以及車輛暫態響應的是彈簧剛性，影響操控性以及轉向特性的是防傾桿以及彈簧剛性。 因此，我們會先根據圈時來調整彈簧剛性，在調整至最佳圈時之後，再根據車手回饋調整防傾桿扭轉剛性，配合賽道配置以及車手感受。

## Slide 29: Tool development

## Slide 30: Tire grip estimation
Linear potentialmeter
GSS
IMU
Sideslip angle
Yaw rate
Suspension model
Steering sensor
Steering sensor
slip angle
displacement
Load
car attitude
Tire model
FY
FX

## Slide 31: Tire load estimation

## Slide 32: Slip angle estimation

## Slide 33: Appendix
Tire data/Suspension mechanism/Set up sheet

## Slide 34: Tire data lat. force

## Slide 35: Tire data cornering stiffness

## Slide 36: Tire data cornering stiffness coefficient

## Slide 37: Tire data lat. force coefficient

## Slide 38: Tire data optimal pressure (Fy)

## Slide 39: Tire data long. force

## Slide 40: Tire data long. force

## Slide 41: Tire data long. force

## Slide 42: Tire data long. force coefficient

## Slide 43: Tire data aligning torque

## Slide 44: Front suspension mechanism

## Slide 45: Rear suspension mechanism

## Slide 46: Suspension set up sheet

## Slide 47: Suspension parameter
front
rear
Notes: 在轉向特性前後平衡(也就是neutral steer)的前提下，我們透過五種彈簧剛性搭配三種防傾桿扭轉剛性，前懸以及後懸各有15種設定，就全車來說就有225種設定。調整參數的流程如前面所述，先從圈時去調整彈簧剛性，在得到最佳圈時後再根據車手反饋調整防傾桿，配合車手開車風格。
在這麼多種的懸吊設定之下，更需要多做試驗來最佳化車輛。 希望可以在今年的試車期，更掌握彈簧剛性以及防傾桿對車輛表現的影響，才能夠最大化車輛表現，並且可以因應不同的賽道，做出及時的懸吊調整。

## Slide 48: Slip angle estimation model

## Slide 49: Load estimation model
: Spring Displacement(m)
: Spring Rate (N/m)
: motion ratio [-]
: Roll Angle (deg)
: Anti-Roll Bar Roll Stiffness (Nm/deg)